## Slide 1
When you open TopSpin it usually looks something like this… there
is no dataset open yet.

## Slide 2
When you click on the “+” next to the folders in the browser pane
it will expand to the next level.

## Slide 3
The first level is the experiment name, the next level is the experiment
number (here, 20).

## Slide 4
The bottom level (usually a “1”) is the processed data for the
experiment – double-click on it and the spectrum will be displayed.

## Slide 5
Often, when you open it the data will look like this… the lines are
out of phase. They should be absorptive, these are dispersive.

## Slide 6
If you choose the Process tab, then the “Adjust Phase” menu, you
will get a number of options for correcting the phase.

## Slide 7
All of the commands can also be typed in to the box at the bottom
of the TopSpin window.

## Slide 8
To expand a region of the spectrum click (and hold) the cursor on
One side then drag the cursor over the region you want expanded.

## Slide 9
You can adjust the vertical scale with the mouse wheel (or scroll-pad)
When you do, you may find that the phase still isn’t quite right.

## Slide 10
Click on the “Adjust Phase” button to enter manual phasing, then click
And hold on the “0” button. Sliding the mouse will adjust the phase.

## Slide 11
The phase is correct when the baseline is flat on either side of the peak
that has a red line on it (referred to as the “pivot point”).

## Slide 12
But you may find that lines away from the pivot point are now out of
phase. Expand the line furthest from the pivot point.

## Slide 13
The rest of the spectrum needs a frequency dependent phase
correction which is done by clicking/holding/dragging the “1”.

## Slide 14
When you are happy with the phasing you need to save the result
by clicking on the save icon (looks like a floppy disk).

## Slide 15
If there is a reference compound (such as TMS) you should now
set it to 0 ppm. This needs to be done before anything else.

## Slide 16
If you select “Pick Peaks” the program will automatically select the
Peaks and enter a mode where you can edit the selection.

## Slide 17
The last piece of processing is baseline adjustment. The automatic
version works quite well using the command abs(n).

## Slide 18
You will find more baseline correction options under the “Advanced”
menu. It’s the one place where the work-flow is out-of-order.

## Slide 19
abs will create default integrals, absn performs baseline correction
but does not create integrals… leaving you to do so manually.

## Slide 20
In integration mode. The first icon along enables you to switch
between the cursor’s integration and expansion modes.

## Slide 21
When the icon is not selected you can expand regions of the
spectrum as usual.

## Slide 22
Sometimes a peak (or multiplet) will give a strange looking integral.
The slope and bias of that integral need to be manually adjusted.

## Slide 23
You can select an integral by right-clicking on it (a menu pops up
with “Select” as an option. Bias is adjusted with the “b” icon.

## Slide 24
Slope is adjusted with the “s” icon. As with phase correction you need
to click and hold on the icon, then drag to make the adjustment.

## Slide 25
When you right click on an integral and select it, you can then right-
-click again to calibrate. There is also a button to select all integrals.

## Slide 26
If you select all the integrals, there is also a button to delete them all
Which is useful if you make a mess and want to start again!

## Slide 27
And again, as with phase correction, you need to save the results
when you’ve finished.